## Slide 1: CarHackingLab
ICSim

## Slide 2: Setup

## Slide 3: Needed Software
Download VMware Player here: https://www.vmware.com/products/workstation-player.html
Download Ubuntu here: https://ubuntu.com/
Follow steps for ICSim here: https://github.com/zombieCraig/ICSim
Resources for this lab:
  The Car Hacker’s Handbook
  https://hackaday.io/project/175126-learn-how-to-hack-a-car-remoticon-workshop
    This workshop is based on the workshop from Hackaday’s remoticon in 2020. If you’re getting stuck, you can also use these resources

## Slide 4: Installation steps
Install VMware Player
After installing and starting VMware, create a new virtual machine and select the downloaded Ubuntu .iso file
Follow the installation steps and leave the default values

## Slide 5: Creating a new Virtual Machine with Ubuntu
Make sure to select your downloaded Ubuntu .iso file
Leave the rest of the options as default, we don’t need special settings for this lab

## Slide 6: ICSim
Open a terminal in Ubuntu
Install git, make, and gcc with ‘sudo apt install git make gcc’
Head over to https://github.com/zombieCraig/ICSim , we want to get the git repo with:
  git clone https://github.com/zombieCraig/ICSim.git
Install needed libraries:
  sudo apt-get install libsdl2-dev libsdl2-image-dev can-utils
Change to directory ICSim, which you just download

## Slide 7: Setting up Virtual CAN Interface
Change to directory ICSim, which you just downloaded and enter following commands:
  make
  ./setup_vcan.sh
  ./icsim vcan0
  ./controls vcan0

## Slide 8: Start ICSim and Controls in Ubuntu

## Slide 9: CAN Messages
In another terminal window, run:
  candump vcan0
You should see the CAN messages of ICSim

## Slide 10: Replay Attack with ICSim

## Slide 11: Replay Attack
Record the CAN messages with:
  candump –L > open_door.log vcan0
  While recording, open the doors using the controller (it’s a bit tricky to open the doors with the controller, so hold the left shift key and press the right or the other way around until the doors open)
Have a look at the dump:
  head –n 10 open_door.log | log2long
Replay the file:
  canplayer –I open_door.log

## Slide 12: Replay Attack (cont.)
If it doesn’t work with opening the doors too well, you can also try it with the speed or turning left/right.

## Slide 13: Find the exact command

## Slide 14: Finding the CAN command that opened the door
Count the lines in your file:
  wc –l open_door.log
Split the log file:
  Split –l open_door.log
If the file is too long or if you get stuck, head over to https://hackaday.io/project/175126-learn-how-to-hack-a-car-remoticon-workshop , download the file content and try it with the 100 lines file mentioned in that workshop